OXYGEN SERVICE

EQUIPMENT HANDLING AND INSTALLATION

- PRE-INSTALL

  - Visually inspected that all items are bagged and labeled “Cleaned for Oxygen Service”

  - Check bags for holes, tears, or any other damages to the bag or the item itself

- HANDLING AND INSTALLATION

- HANDLE ALL ITEMS WITH CARE

- Do not remove items from packaging until ready to be installed

- All assembly and installation tools should be clean of any oil, dirt, or any other hydrocarbons

- Wash Hands (Glove use not recommended)

- Use Oxygen compatible lubricants only

- Cut tubing with tubing cutter only (no grinders, saws, files)

- Do not use any tools that create shavings, particles, or oil

  - POST INSTALLATION

    - Purge complete system with Dry Nitrogen

    - Do Not Use any solvents in assembled system